## Slide 1
Boolean Matching in Logic synthesis
Advanced Logic Design (CSE-524)
Presented by:
Sabbir Mahmud Afridi
MS Session 2022-202_3
Roll: SH-2_3_34
University of Dhaka

## Slide 2: Outline
Logic Synthesis
Technology Mapping
  Example of Technology Mapping
Cell Library
Negation, Permutation on Variables
Equivalence of functions
Shannon’s expansion
  Example
Boolean Matching
  Algorithm
  Flowchart
Application of Boolean Matching

## Slide 3: Logic Synthesis
Logic synthesis is the process of converting a high-level design or description of a digital circuit into a list of basic logic gates (like AND, OR, NOT) that can be physically built in hardware.
Goal
Maximize Speed
Minimize Power
Minimize Chip/Board Size

## Slide 4: Logic Synthesis Procedure

## Slide 5: Technology Mapping
• Technology mapping is the phase of logic synthesis when gates are selected from a technology library to implement the circuit.
• Technology mapping is normally done after technology independent optimization.
In Another sense
Technology mapping is the process of expressing a given Boolean network in terms of library gates (for standard cells) or look-up tables.

## Slide 6: Cell Library/Standard Cell
A collection of low-level logic function such as AND, OR, INVERT, flip-flops, latches, and buffers.

## Slide 7: Why Technology Mapping?
Straight implementation may not be good.
  For example, F = abcdef as a 6-input AND gate cause a long delay.
Gates in the library are pre-designed
They are usually optimized in terms of area, delay, power, etc.
Moreover we may don't have available gates in the Library
The circuit on the top of the figure shows a combination of different logic gates (AND, OR, NOT, etc.) connected in a certain way to perform a specific function.
The circuit on the bottom illustrates how the original design can be optimized by replacing the complex gates with more standardized gates that are available in the library.

## Slide 8: Where is Technology Mapping?
Simplification of logic equations
  Reduce number of literals (and operands)
Synthesis
  Map logic equations to gates (AND, OR, etc)
Gate-level optimization
  Replace OR-NOT by NOR, for example : delay, power, area
Technology mapping
  Map from gates to technology library
  FPGA, TTL chips, standard cells, etc.

## Slide 9: Mapping to NAND and NOR gates

## Slide 10: Technology Mapping
There are Two Types of Technology Mapping:
Structural Matching
  Structural matching involves mapping a high-level design (such as a Boolean expression or a logic circuit) directly to the structure of available hardware elements.
  It focuses on maintaining the actual structure and organization of the hardware components (e.g., gates, multiplexers, flip-flops, etc.) while trying to meet the performance and resource constraints.
  In structural matching, the design’s functionality is preserved, but the mapping is done in a way that directly reflects the available physical structures and hardware components.
Boolean Matching
  Boolean matching focuses on matching Boolean expressions or logic functions to optimized sets of logic gates or blocks.
  This type of mapping is primarily concerned with the logical equivalence of functions rather than the physical layout or the exact hardware structure.
  The goal is to find a set of gates that can implement the Boolean functions efficiently. It usually involves simplifying the logic functions using techniques like Boolean algebra or Karnaugh maps before mapping them to the available technology.

## Slide 11: Structural Mapping
Decompose:
  Subject and pattern graphs into common terms
  - NAND/NOR
  Could have multiple representations - Decomposition is not canonical
Make DAGs into trees
  Make fanouts into primary outputs
  Duplicate logic
  Tree matching and covering run in linear time

## Slide 12: Structural Mapping
Structural Mapping Problems
Trees only:
  No optimization across fanout nodes
  No XOR gates
Imperfect matching. Example: f= xy+x′y′+y’z
g= xy+x′y′+xz
Different structure, same function
Solution: Boolean matching and covering

## Slide 13: Equivalence of functions
Equivalence of two functions defined under:
Negation of input variables
Permutation of input variables
Negation of output

## Slide 14: Negation of Input Variables

## Slide 15: Permutation of Input Variables

## Slide 16: Negation of Output

## Slide 17: Equivalence of Functions
NPN-Equivalent:
- Equivalent under:
      Input Negation
      Input Permutation
      Output Negation

## Slide 18: Equivalence of Functions
NPN-Equivalent:
- Equivalent under:
      Input Negation
      Input Permutation
      Output Negation

## Slide 19: Minterm Expansion

## Slide 20: Maxterm Expansion

## Slide 21: Shannon Decomposition/Expansion

## Slide 22: Shannon Decomposition/Expansion

## Slide 23: Shannon Decomposition/Expansion

## Slide 24: Boolean Matching Algorithm

## Slide 25: Boolean Matching Algorithm
Generate functions of all possible permutations and combinations on the inputs of A.
Generate functions of all possible permutations and combinations on the inputs of B.
Try to find if any of the outcomes of A match with the outcome of B.
If matching is found, then we can say that an instance of A can be modeled with an instance of B.

## Slide 26: Possible Combination
Variables of an n-variable function can be permuted in n! ways and complemented in ways; thus the total number of possible combinations are .

## Slide 27: Computing NP-Representative
For example, let

## Slide 28: Computing NP-Representative

## Slide 29: Computing NP-Representative

## Slide 30: Computing NP-Representative

## Slide 31: Computing NP-Representative

## Slide 32: Conclusion
Although checking of functional equivalence of two functions is NP-hard problem.
Boolean matching eases this task better than other techniques like
K-map or Quin-Maclauskys.
It is used practically while logic synthesis for commonly used circuits.